## Slide 1: Troubleshooting SDNs
Peyman Kazemian

## Slide 2: Why SDN Troubleshooting
SDN decouples software (control plane) from hardware (data plane).
  Opens doors for innovation in networks.
  More competition in the industry.
  Brings down the capex.
  Makes network management task easier and hence reduce opex.
    SDN software stack is a complex, asynchronous distributed system which introduces new troubleshooting challenges.
    Software from one vendor and hardware from the other vendor. What will happen when things break? Who to blame?

## Slide 3: Why SDN Troubleshooting
SDN gives us a unique opportunity for systematic troubleshooting.
  Decouples control plane from data plane.
  State changes pushed from a logically centralized location.
  Easier access to the state of the network.
  Provides clear abstraction for control plane functionality.
  Richer troubleshooting techniques.

## Slide 4
Firmware
Firmware
Firmware
Network OS
Network Hypervisor
App
App
App
Logical View
Physical View
Device State
Hardware
Policy
Bug = Mistranslation between different layers
==
SDN Architecture
Notes: SDNs defines a clear layering of control and data plane which help us to debug the networks.
The interface code of Each layer translates data from the higher layer to the lower layer. It also presents some data from lower layer to higher layer.
Review the layering structure
At any point in time the observable behavior of hardware should match the policy.

## Slide 5: Reactive Troubleshooting of SDNs
One possible Binary Search to detect where error happens reactively.
[Operator Intent]
Logical View
Device State
“Apps”
NetHypervisor
Firmware
Hardware
NetOS
Physical View
Policy
[Actual Behavior]
=
?
=
?
=
?
=
?
=
?
No
Yes
No
No
Yes
No
Yes
Yes
No

## Slide 6: Proactive Troubleshooting of SDNs
One possible Binary Search to detect where error happens proactively.
[Operator Intent]
Logical View
Device State
“Apps”
NetHypervisor
Firmware
Hardware
NetOS
Physical View
Policy
[Actual Behavior]
=
?
=
?
=
?
=
?
No
No
Yes
No
Yes
No
=
?
Yes
No

## Slide 7: Research works on sdn troubleshooting

## Slide 8: Troubleshooting SDNs
[Operator Intent]
Logical View
Device State
“Apps”
NetHypervisor
Firmware
Hardware
NetOS
Physical View
Policy
[Actual Behavior]
=
?
=
?
=
?
=
?
=
?
=
?
NDB (Where is the debugger for my software defined network, HotSDN’12)
ATPG: (Automatic Test Packet Generation, CoNEXT’12)

## Slide 9: Troubleshooting SDNs
[Operator Intent]
Logical View
Device State
“Apps”
NetHypervisor
Firmware
Hardware
NetOS
Physical View
Policy
[Actual Behavior]
=
?
=
?
=
?
=
?
=
?
=
?
AntEater (Debugging the dataplane with AntEater, Sigcomm’11)
HSA (Header Space Analysis: static checking for networks NSDI’12)
VeriFlow (Verifying Network-wide invariants in real time, HotSDN’12)

## Slide 10: Troubleshooting SDNs
[Operator Intent]
Logical View
Device State
“Apps”
NetHypervisor
Firmware
Hardware
NetOS
Physical View
Policy
[Actual Behavior]
=
?
=
?
=
?
=
?
=
?
=
?
OFRewind (Enabling record and replay troubleshooting for networks, ATC’11)
NICE (a NICE way to test OpenFlow applications, NSDI’12)

## Slide 11: Troubleshooting SDNs
[Operator Intent]
Logical View
Device State
“Apps”
NetHypervisor
Firmware
Hardware
NetOS
Physical View
Policy
[Actual Behavior]
=
?
=
?
=
?
=
?
=
?
=
?
Bi-Simulation (What, Where and When: Software Fault localization for SNDs, UC Berkeley tech report)

## Slide 12: Troubleshooting SDNs
[Operator Intent]
Logical View
Device State
“Apps”
NetHypervisor
Firmware
Hardware
NetOS
Physical View
Policy
[Actual Behavior]
=
?
=
?
=
?
=
?
=
?
=
?
RIB == FIB? Compare device state as reported by against the actual bits and bytes in TCAMs, etc.

## Slide 13: What else is needed?

## Slide 14: Policy Expression Language
Rarely the policies are maintained anywhere, except in the mind of network admins!
Systematic troubleshooting requires such clear policy description.
Easy-to-use, expressive and standard network policy description language.

## Slide 15: Better Troubleshooting Tools
Not just detect where the problem is, but also find its root cause -- automaticaly.
  Some of these tools can partially do that.
Challenges:
  What Information is needed?
    Packet history (NDB)?
    Control message history (OFRewind)?
    “Logic” behind control/data plane?
    …
  What is the expected output?
    The sequence of events that lead to the error?
    The exact (relevant) state of control software and hardware?
    Looks like a mix of networking and symbolic execution and formal verification.

## Slide 16: Automated Troubleshooting
Automatically run the search through different layers to pinpoint the error.
  Example: a complete system could do
    Real time monitoring of data plane with test packets.
    Real time checking of network policy against control messages.
    Problem in data plane (e.g. link down, congestion, etc)
      Report it to a control application to reroute traffic around the troubled area.
    Problem in control plane:
      Prevent the change from hitting data plane.

## Slide 17: Policy Driven SDN
Use these techniques in reverse – try to derive correct state/configurations from the policy.
Challenges:
  A policy can be implemented in zillion ways. How to reduce the search space?
  Avoid conflicting implementation.
  What is the correct level of human involvement?

## Slide 18: References
A. Wundsam, D. Levin, S. Seetharaman, and A. Feldmann. OFRewind: enabling record and replay troubleshooting for networks In Proceedings of USENIX- ATC 2011.
H. Zeng, P. Kazemian, G. Varghese, and N. McKeown. Automatic Test Packet Generation. In Proceedings of CoNEXT 2012, Nice, France, December 2012.
A.Khurshid, W.Zhou, M.Caesar and P.B.Godfrey. Veriflow: verifying network-wide invariants in real time. In Proceedings of HotSDN 2012.
P. Kazemian, G. Varghese, and N. McKeown. Header space analysis: static checking for networks. In Proceedings of NSDI’12, 2012.
N. Handigol, B. Heller, V. Jeyakumar, D. Mazie ́res, and N. McKeown. Where is the debugger for my software- defined network? In Proceedings of HotSDN 2012.
M.Canini, D.Venzano, P.Peresini, D.Kostic ́ and J.Rexford. A NICE way to test openflow applications. In Proceedings of NSDI 2012.
H. Mai, A. Khurshid, R. Agarwal, M. Caesar, P. B. Godfrey, and S. T. King. Debugging the data plane with anteater. In Proceedings of SIGCOMM 2011
C. Scott, A. Wundsam, K. Zarifis and S. Shenker. What, where and when: Software fault localization for SDN. UC Berkeley technical report.